## Slide 1
Boosting ADAS Camera Robustness
Yuval | Shahaf | Guy

## Slide 2
Novel Approach: Simulating Real-World Obstacles
Motivation & Specifications
Improve ADAS camera robustness by simulating lens contamination (mud, droplets, dirt) to train object detection models under adverse conditions.
Key Contributions
Application of KITTI dataset with realistic multi-type lens contamination.
Data augmentation simulating real-world environmental conditions.
Establishing a benchmark for ADAS performance under lens contamination.

## Slide 3
Previous Related Work
Title / Year
Task
Methods
Data
Results
Relation to Project
Effect of Droplet Contamination on Camera Lens Surfaces (2025)
Quantify droplet impact on image quality + detection
MTF/MTF50 + YOLOv8x mAP under controlled droplets
Controlled lens/cover glass; varying droplet coverage; hydrophilic vs hydrophobic
Small-object mAP can drop up to ~90%; hydrophilic worse
Motivation + guides severity/coverage parameters for our synthetic contamination
Enhancing ADAS Sensor Vision in Rain (2024)
Check if retraining helps under droplet images
Train YOLOv3/YOLOv4 on droplet-influenced images; compare to pretrained
Wind-tunnel rain simulation; single-class (stop sign)
Retrained models outperform pretrained under droplets
Supports training/evaluating on contaminated data (we use a simplified pipeline)
Impact of Raindrops on Camera-Based Detection (2024)
Analyze which raindrop factors hurt detection most
Raindrop-type/density analysis; propose YOLO-RA; optional SR3+YOLO-RA
BDD100K-based rainy data with raindrop categories
Density/coverage most damaging; mitigation improves metrics
Helps choose what to vary (density/coverage) in our contamination generator (no need to implement their model)

## Slide 4
Building the Contaminated Dataset
1
Dataset Creation
Base: KITTI object detection images.
Contaminations: mud, dirt, water droplets.
Labels: same as KITTI (bounding boxes).
2
Generation Techniques
Alpha-blended contamination textures.
Randomized contamination levels and placement for realism.
3
Exploratory Data Analysis (EDA)
Class distribution consistent with original KITTI.
Balanced contamination distribution across types.
Visualizing the impact of contamination:

## Slide 5
Baseline Performance & Analysis
Baseline Model: Pretrained YOLOv8
Utilized a pretrained YOLOv8 model on KITTI, with minimal adaptation to contaminated images initially.
Observation: Significant Accuracy Drop
Performance reduced with heavy contamination, highlighting the need for specialized training.
Error Analysis: False Negatives
Mostly on objects partially occluded by contamination, confirming the necessity for data augmentation.

## Slide 6
Project Roadmap & Next Steps
1
Dataset Generation
-week 9-
Description: Create full contaminated KITTI dataset (mud, droplets, mixed).
Outcome: Complete labeled dataset for training.
2
Model Training
-week 10-
Description: Fine-tune YOLOv8 on the newly contaminated dataset.
Outcome: Improved detection under various contamination scenarios.
3
Evaluation
-week 11-
Description: Evaluate model on both contaminated and clean images.
Outcome: Quantitative performance analysis and benchmark.
4
Optimization
-week 12-
Description: Adjust data augmentation and hyperparameters.
Outcome: Maximized accuracy under all contamination types.
5
Final Presentation
-week 13-
Description: Prepare comprehensive slides & visualizations.
Outcome: Showcase results and future implications.